## Slide 1: Configure Arduino Micro for AC-DC Testing
Dr. Robert Sheehan Senior Technical Officer Dept. of Physics University College Cork 11 – 1 – 2021
Notes: Buy a usb oscilloscope for people – balls to that, AM can sample
Ensure that we have spares of components to send out to people
Send all components at the same time

## Slide 2: Arduino Micro
Arduino Micro (AM) is a development board based on the ATmega32u4 microcontroller.
Full details around the board’s technical specs can be obtained at the supplier website: https://ie.farnell.com/arduino/a000053/arduino-micro-dev-board/dp/2285194?ost=2285194#
Full details around the board’s technical specs can be obtained from the board data sheet (this one is in pdf format, therefore better): http://www.farnell.com/datasheets/1685581.pdf

## Slide 3: Arduino Micro Power
Arduino Micro can be powered via the micro USB connection or with an external power supply.
External (non-USB) power can come either from a DC power supply or battery.
External power supply must be between 7V and 12V to ensure correct operation of board.
When board is powered correctly it is able to supply regulated 5V DC and 3.3V DC as well as acting as ground.
The DC supply is limited in current, max current output is less than 50 mA.

## Slide 4: Arduino Micro Power
In this diagram ( created using Fritzing https://fritzing.org/ )
Two rails are connected to GND
One rail is connected to 3.3V DC supply
One rail is connected to 5.5V DC supply
It is assumed that board is powered through USB connected to a PC
GND
GND
3.3V
5V

## Slide 5: Arduino Micro Pinout
As well as the GND, 3.3V and 5V power pins Arduino Micro has several pins that can be used for DC testing
  Pins A0 – A5 are analog inputs
    they can be used to read DC voltage in the range 0V to 5V
    Voltage values outside the range [0, 5] will not be read
  Pins D2 – D13 are digital outputs
    they can be set to digital ON (5V) or digital OFF (0V)
  Pins D4 – D6, D9, D10, D12, D13 are digital pulse width modulation (PWM) outputs
    they can be used to generate a train of variable width pulses
    PWM can be converted to quasi-analog DC signal in the range [0, 5]
  Full pinout shown on next slide
  Note that some pins have multiple functions (We’ll keep it simple for now. )

## Slide 6: Arduino Micro Pinout
Analog In
Digital Out

## Slide 7: Arduino Micro Programming
Arduino Micro must be programmed using a variant of the C programming language
Instructions for the board are written in a file called a sketch
The sketch is then uploaded to the board and the board executes the instructions
It is possible to interact with the board via text based Serial communications console after instructions are uploaded

## Slide 8: Arduino Micro Programming
Arduino supplies an integrated development environment (IDE) that can be used to edit sketches and upload them to an Arduino board
Arduino IDE comes pre-packaged with a set of libraries written for Arduino boards
Arduino IDE can be obtained free of charge from https://www.arduino.cc/en/software
Arduino also have an online language reference library https://www.arduino.cc/reference/en/
Sketches and LabVIEW code enabling all testing required for PY2108 is available at https://github.com/rnsheehan/ArdForPY

## Slide 9: Arduino Micro Programming
Useful links:
Sketches and LabVIEW code enabling all testing required for PY2108: https://github.com/rnsheehan/ArdForPY
Introduction to Arduino: https://learn.sparkfun.com/tutorials/what-is-an-arduino/all
Installing Arduino IDE: https://learn.sparkfun.com/tutorials/installing-arduino-ide
Installing an Arduino Library: https://learn.sparkfun.com/tutorials/installing-an-arduino-library
Installing Arduino Board Definitions: https://learn.sparkfun.com/tutorials/installing-board-definitions-in-the-arduino-ide

## Slide 10: Arduino Micro and DC Characterisation
Configure Arduino Micro for DC Output
Circuit for Semiconductor Diode Characterisation
Circuit for npn BJT Characterisation

## Slide 11: Arduino Micro PWM Output
Arduino Micro can be configured to supply Pulse Width Modulated (PWM) output
PWM outputs a train of pulses of variable duty cycle with period T = 0.002 s (f = 490 Hz)
By varying the pulse duty-cycle you vary the average value of the output voltage over each period
PWM is available on Pins D4 – D6, D9, D10, D12, D13
Notes: Put in a picture of the PWM output here

## Slide 12: Arduino Micro PWM Output
PWM
PWM
PWM

## Slide 13: Arduino Micro DC Output
Arduino Micro can be configured to supply DC output
By applying an RC filter (R = 1 kW, C = 100 mF) to the PWM output you can convert the AC PWM signal to a quasi-DC signal
The level of the quasi-DC signal can be varied by changing the PWM duty cycle.
Duty Cycle | Bit Value | Average Voltage / V
0 | 0 | 0
25 | 64 | 1.243
50 | 127 | 2.45
75 | 191 | 3.7
100 | 255 | 5
Notes: Add a slide that talks about how this is then controlled using software

## Slide 14: Arduino Micro DC Output
To obtain a desired average voltage of Vd from PWM choose PWM duty-cycle dc = int( 51 * Vd )
Notes: Here is the calculation that proves the average of the PWM output equals the DC output

## Slide 15: Arduino Micro DC Output 1 Ch
Pin 9 PWM
PWM -> DC
PWM can be converted to DC by application of LPF R = 1kW, C = 100 mF
Notes: Add notes to this diagram so people know what the hell you’re talking about

## Slide 16: Arduino Micro DC Output 1 Ch
Pin 9 PWM
PWM -> DC
PWM can be converted to DC by application of LPF R = 1kW, C = 100 mF
Notes: Add notes to this diagram so people know what the hell you’re talking about

## Slide 17: Arduino Micro DC Output 1 Ch
Once the RC filter is in place the voltage level can be altered via Serial Interface to the board after sketch DCWriteRead.ino has been uploaded to the board
The sketch DCWriteRead.ino is available at https://github.com/rnsheehan/ArdForPY
The output voltage level is altered by calling the internal Arduino function analogWrite, see https://www.arduino.cc/reference/en/language/functions/analog-io/analogwrite/ for details
The arguments to the function are the pin being used and the duty-cycle value, see code snippet on next slide for details

## Slide 18: Arduino Micro DC Output 1 Ch
Sample input: b2.7 /* tell board to output 2.7V from channel B */
Compute duty-cycle to get desired average voltage In this case DC = 138
Change PWM duty-cycle

## Slide 19: Arduino Micro DC Output 1 Ch
You can now vary the DC voltage being output by the board, however, you are limited in current to approx. 40 mA.
To overcome this limitation add a unity gain current amplifier (npn transistor) to your board.
In doing so you will amplify your current output by a factor b ~ 100
The transistor can be powered by connecting the 5V output of the Arduino Micro to the BJT collector terminal.
Current is amplified by connecting DC signal to the BJT base terminal
Amplified current can be put through DUT connected to BJT emitter terminal

## Slide 20: Arduino Micro Diode Characterisation
Vin
Consider characterisation of semiconductor diode
AM can generate DC signal 0 <= Vin <= 5V after
passing through RC LPF with R = 1kW, C = 100 mF
Current is amplified by passing DC signal through BJT
Actual current passing through diode for given input DC bias can be found by measuring bias across known resistor R ~ 10 W, Id = A0 – A1 / R
Actual bias across diode can be measured directly using AM Vd = A1
By sweeping the value of Vin and measuring Id and Vd for each value the diode characteristic curve can be measured.

## Slide 21: Arduino Micro Diode Characterisation
Pin 9 PWM
Vin
A0
A1
Gnd
+5V
Layout of diode characterisation circuit on breadboard
Vin specified by DCWriteRead.ino
Command: a<vin> <vin> is some number in the range [0, 5]
A0, A1 measured by board
Command: l ( ``ell’’ for léigh, lis, lesen etc)

## Slide 22: Arduino Micro Diode Characterisation
Possible to implement DC sources on AM
+5V is supplied by AM, no external
power-supply needed
Current amplifiers required to ensure sufficient current is available.
Measurement of biases enabled through Analog Inputs A0 – A5 on board
Results as expected for R = 10 W and diode FR1001
Chart: Automated Diode IV Measurement Using AM
| 0.28000000000000003 | 0.56000000000000005 | 3 | 6.3514285713999996 | 11.17 | 17.739999999999998 | 22.97 | 30.727142857099999 | 37.707142857100003 | 45.031428571399999 | 54.947142857099998 | 63.122857142900003 | 70.66 | 79.180000000000007 | 86.645714285699995 | 94.89 | 103.34 | 110.74 | 118.83857142860001 | 127.1457142857 | 136.91999999999999
 | 0.3931 | 0.5062 | 0.5509 | 0.5914 | 0.6263 | 0.64863 | 0.6717 | 0.6905 | 0.7038 | 0.7178 | 0.73036 | 0.7415 | 0.7506 | 0.7576 | 0.766 | 0.7722 | 0.7771 | 0.7841 | 0.7911 | 0.7967 | 0.8016

## Slide 23: Arduino Micro Diode Characterisation
Pin 9 PWM
PWM -> DC
This is the schematic offered up by
Fritzing when I made the breadboard diagram.

## Slide 24: Arduino Micro DC Output 2 Ch
Since there are multiple independent PWM channels you can have multiple independent DC sources
You just need to add RC LPF and BJT to each PWM output that you want
For PY2108 two DC sources is sufficient
In my implementation I have chosen pin 9 (labelled ``a’’ in the sketch) and pin 6 (labelled ``b’’ in the sketch)

## Slide 25: Arduino Micro DC Output 2 Ch
Pin 9 PWM
PWM9 -> DC1
Pin 6 PWM
PWM6 -> DC2
Independent DC output can be obtained on multiple PWM channels R = 1kW, C = 100 mF
For current amplification you will need BJT powered by +5V on each
GND

## Slide 26: Arduino Micro DC Output 2 Ch
Pin 6 PWM
PWM9 -> DC1
Pin 9 PWM
PWM6 -> DC2
Independent DC output can be obtained on multiple PWM channels R = 1kW, C = 100 mF
GND

## Slide 27: Arduino Micro BJT Characterisation
Consider characterisation of npn transistor Qc
DC signals can be generated by channels a (PWM9) and b (PWM6). Current on those channels is amplified by UGA Qa, Qb each powered by AM +5V output
To obtain characteristic of Qc choose Rb, Rc st Rb ~ 20 Rc
Apply a constant bias to base of Qc, i.e. fix Vinb to get constant current through Rb -> Ib = (A2 – A3) / Rb
Sweep bias at collector Qc, vary Vina to get variable current through Rc, Ic = (A0 – A1) / Rc
Measure collector-emitter bias Vce = A1
Can then obtain plot Ic versus Vce for different Ib values

## Slide 28: Arduino Micro BJT Characterisation
Pin 6 PWM
Vina
Pin 9 PWM
Vinb
GND
Rc
Rb
Layout of BJT characterisation circuit on breadboard
Vinb specified by DCWriteRead.ino
Command: b<vinb>
Vina specified by DCWriteRead.ino
Command: a<vina>
<vin*> is some number in the
range [0, 5]
A0, A1, A2, A3 measured by board
Command: l ( ``ell’’ for léigh, lis, lesen etc)

## Slide 29: Arduino Micro BJT Characterisation
Possible to implement two DC sources on AM
Fix Vb while sweeping Vin
+5V is supplied by AM, no external
power-supply needed
Current amplifiers Qa, Qb required to ensure sufficient current is available. Measurement of biases enabled through Analog Inputs A0 – A5 on board

## Slide 30: Arduino Micro BJT Characterisation
Pin 6 PWM
PWM9 -> DC1
Pin 9 PWM
PWM6 -> DC2
Schematic of BJT board output by Fritzing
GND

## Slide 31: Arduino Micro and AC Characterisation
Configure Arduino Micro and SparkFun MiniGen for AC Output
Ensure Correct Operation of SparkFun MiniGen
LRC Filter Characterisation
OpAmp Characterisation

## Slide 32: Arduino Micro AC Output
Arduino Micro cannot output an AC signal on its own
It can communicate with an external device that can generate a signal
The device we are using is called the SparkFun MiniGen
It outputs a 1 Vpp signal at DC offset of 1.65 V

## Slide 33: Arduino Micro AC Output
Further details on the SparkFun MiniGen can be found here: https://learn.sparkfun.com/tutorials/minigen-hookup-guide
Details relating to SparkFun MiniGen software libraries can be found here: https://github.com/sparkfun/MiniGen

## Slide 34: Arduino Micro AC Output
AM speaks with SFMG via communications protocol known as Serial Peripheral Interface (SPI), see https://en.wikipedia.org/wiki/Serial_Peripheral_Interface for details
Code exists to control operation of the SparkFun MiniGen, see https://github.com/rnsheehan/ArdForPY for details
Control over the SparkFun MiniGen requires SPI pins on Arduino Micro

## Slide 35: Arduino Micro Pinout
Analog In
Digital Out
Here are the usual digital and analog pins on the AM

## Slide 36: Arduino Micro Pinout
3.3V
D10
MOSI
Gnd
SCK
Here are the SPI pins on the AM

## Slide 37: SparkFun MiniGen Connections
SparkFun MiniGen is supplied without headers Your friendly neighbourhood technical officer has soldered headers on for you There are 8 connections of interest 1. GND * 2 = Ground at Arduino Micro
2. VIN = Power Supply input from Arduino Micro 3.3V output
3. Output + = Signal output, 1 Vpp + Vin/2 DC offset
4. Output - = Connect to GND
5. SCLK = Serial Clock Input, connect to Arduino Micro SCK output
6. SDATA = Serial Data Input, connect to Arduino Micro MOSI output
7. FSYNC = Chip Select Input, connect to Arduino Micro D10
Ensure connections between Arduino Micro and SparkFun MiniGen are made correctly! Default output after uploading sketch SigGenWriteRead.ino will be 1 kHz sine wave

## Slide 38: SparkFun MiniGen Connections
SparkFun MiniGen | Arduino Micro
Gnd | Gnd
Vin | 3.3V
Output- | Gnd
SCLK | SCK
SDATA | MOSI
FSYNC | D10
Output+ | Device Under Test
Gnd
Vin
3.3V
SCLK
SDATA
FSYNC
Gnd
DUT / Osc
Gnd
D10
Gnd
SCK
MOSI
Check that device is working before making connections on breadboard using female-female connector cables All Gnd can be shorted together

## Slide 39: SparkFun MiniGen Connections
SparkFun MiniGen | Arduino Micro
Gnd | Gnd
Vin | 3.3V
Output- | Gnd
SCLK | SCK
SDATA | MOSI
FSYNC | D10
Output+ | Device Under Test
Can set-up long term on two breadboards
DUT must be grounded to AM Gnd, same as SFMG
Measurements to take place through analog inputs A0 – A5
DUT
Gnd

## Slide 40: SparkFun MiniGen Sketch
The sketch SigGenWriteRead.ino can be used to change frequency being output by SFMG and also to measure max values on channels A0 and A1
The sketch is available at https://github.com/rnsheehan/ArdForPY
Interaction between the AM and the SFMG is managed by this sketch through Serial comms
Command w<freq> is used to alter frequency output by SFMG, e.g. w33500 tells the SFMG to output at frequency 33.5 kHz
Command r is used to read the max input values on A0 and A1

## Slide 41: SparkFun MiniGen Operation Test
The easiest way to check if the SFMG is operating correctly is to connect output+ to an oscilloscope and observe the wave being generated by the board.
If everything is working correctly you should see a 1 Vpp sine wave at frequency 1 kHz
It should be possible to change the frequency of the wave using the Serial monitor and further confirm that everything is in good working order.
However, given that you probably don’t have access to an oscilloscope we must proceed differently.

## Slide 42: SparkFun MiniGen Operation Test
I will see if I can implement code that enables accurate sampling at low frequency ~ 50 Hz, 100 Hz
To measure a sine wave of frequency f we must sample at frequency >= 2 f
I will start looking at the code and see what I can come up with.

## Slide 43: LRC Characterisation
A0
A1
Set up the RLC filter as usual
Connect input to A0 and output to A1
Recall the signal from SFMG is 1 Vpp sine wave offset by 1.65V
A0, A1 will see a signal, but AM is not able to accurately sample it
AM can only read signal [0, 5]
Add DC block to input in order to prevent DC offset affecting output
Measure response by using AM to measure max{A0} – min{A0} and max{A1} – min{A1}

## Slide 44: LRC Characterisation
Set up the RLC filter as usual
Connect input to A0 and output to A1
Recall the signal from SFMG is 1 Vpp sine wave offset by 1.65V
A0, A1 will see a signal, but AM is not able to accurately sample it
AM can only read signal [0, 5]
Add DC block to input in order to prevent DC offset affecting output
Measure response by using AM to measure max{A0} – min{A0} and max{A1} – min{A1}

## Slide 45: OpAmp Characterisation
Separate +/- 9V power supply required to ensure AM+SFMG can characterise op-amp circuit
+9V
-9V
Gnd

## Slide 46: Inverting OpAmp Characterisation
A0
A1
Set up the inverting amplifier as usual
Connect input to A0 and output to A1
Recall the signal from SFMG is 1 Vpp sine wave offset by 1.65V
A0 will see a signal, but AM is not able to accurately sample it
A1 will see no signal because signal has been inverted
AM can only read signal [0, 5]
Add DC block to input in order to prevent DC offset affecting output

## Slide 47: Inverting OpAmp Characterisation
A0
A1
A0 is in range [0, 5], AM can measure max and min values of signal
A1 is in range [-5, 0], AM cannot see this signal will always return 0 V
Here R1 = R2 = 1 kW -> Vout = -Vin
No DC block at input

## Slide 48: Inverting OpAmp Characterisation
A0
A1
A0 is in range [0, 5], AM can measure max and min values of signal
A1 is in range [-1, 1], AM can see signal > 0
If you add DC block (C = 1 mF) then you can test the Inverting amplifier
Here R1 = R2 = 1 kW -> Vout = -Vin

## Slide 49: Non-Inverting OpAmp Characterisation
A0
A1
Set up the non-inverting amplifier as usual
Connect input to A0 and output to A1
Recall the signal from SFMG is 1 Vpp sine wave offset by 1.65V
A0 will see a signal, but AM is not able to accurately sample it
A1 will see also signal because signal has not been inverted
AM can only read signal [0, 5]
R vals must be chosen st Voutmax < 5 V
Use of DC block can enable wider range of R vals to obtain larger gain

## Slide 50: Non-Inverting OpAmp Characterisation
A0
A1
A0 A1 are both in range [0, 5], AM can measure max and min values of signal
Here R1 = R2 = 1 kW -> Vout = 2Vin
No DC block at input

## Slide 51: Non-Inverting OpAmp Characterisation
A0
A1
Can only measure on [0, 5] but could get higher amplification since no DC offset
Here R1 = R2 = 1 kW -> Vout = 2Vin
DC block at input allows wider choice of R vals to get higher gain

## Slide 52: Arduino Micro DC Sketch

## Slide 53: Arduino Micro DC Sketch
DCWriteRead.ino (https://github.com/rnsheehan/ArdForPY ) can be uploaded to the Arduino Micro to enable DC measurements
The sketch comprises four sections
  preamble
  setup
  loop
  function definitions

## Slide 54: Arduino Micro DC Sketch
Preamble
  Define constants used throughout the code
  Define commands that tell Arduino Micro to perform some action
  Constants and commands have been made consistent between DC and AC sketches
  Commands are kept simple: write or read
  To keep things simple I have defined 5 commands
    AC read ‘r’
    AC write ‘w’
    DC read ‘l’
    DC write from channel A ‘a’
    DC write from channel B ‘b’
  If anything other than these commands is input an error is thrown

## Slide 55: Arduino Micro DC Sketch
Setup
  Tell the board what each of the pin modes are for this sketch
    Pinmode is a built-in command for the Arduino IDE
    https://www.arduino.cc/reference/en/language/functions/digital-io/pinmode/
  Set the baud rate for Serial comms
    https://www.arduino.cc/reference/en/language/functions/communication/serial/begin/
    It’s possible that baud rate can be optimised, but who has the time?

## Slide 56: Arduino Micro DC Sketch
Loop
  Main operating loop for the board
  Loop is written such that it sits and waits for you to enter one of the commands before doing anything
  In the case of DCWriteRead.ino there are only three valid inputs
    readAngStr = l: print current measured voltages from Analog inputs A0 – A5
    writeAngStrA = a<val>: output DC voltage of level <val> from channel A
      E.g. a2.6: output 2.6V DC from channel A
    writeAngStrB = b<val>: output DC voltage of level <val> from channel B
      E.g. a1.234: output 1.234V DC from channel B
    <val> should be a numeric string in the range [0,5], code will force it to either endpoint otherwise
  Any other input will result in printing of ERR_STRING defined preamble
  Arduino IDE has built-in string processing capability
    https://www.arduino.cc/reference/en/language/variables/data-types/stringobject/

## Slide 57: Arduino Micro DC Sketch
Function Definitions
  Functions are defined after loop, no need for forward declaration
  Only one function is used in DCWriteRead: analogVoltageRead
    analogVoltageRead converts the bit-reading at the analog input pin to a voltage value
    analogVoltageRead uses built-in analogRead function
      https://www.arduino.cc/reference/en/language/functions/analog-io/analogread/
  The other function defined in DCWriteRead is not called because is not applicable to the Arduino Micro, but is applicable for the ItsyBitsyM4.

## Slide 58: Arduino Micro DC Sketch
Once the sketch has been uploaded the commands a<val>, b<val>, l can be used to control the device
One way is to open a Serial monitor that talks to the board, using Arduino IDE (Tools -> Serial Monitor) or Putty
The other is to open Serial monitor via LabVIEW
  This has the advantage of enabling data parsing and storage ( the Arduino Micro is a Read-Only file system so it cannot create files )
  AM_DC_Test.vi contains all the code needed to implement component characterisation
    Write vi, Read vi, String Processing, Data Formatting etc
    Diode and BJT characterisation loops have been implemented

## Slide 59: Arduino Micro Programming
Arduino IDE can be obtained free of charge from https://www.arduino.cc/en/software
Arduino also have an online language reference library https://www.arduino.cc/reference/en/
Introduction to Arduino: https://learn.sparkfun.com/tutorials/what-is-an-arduino/all
Installing Arduino IDE: https://learn.sparkfun.com/tutorials/installing-arduino-ide
Installing an Arduino Library: https://learn.sparkfun.com/tutorials/installing-an-arduino-library
Installing Arduino Board Definitions: https://learn.sparkfun.com/tutorials/installing-board-definitions-in-the-arduino-ide

## Slide 60: Arduino Micro AC Sketch

## Slide 61: Arduino Micro AC Sketch
SigGenWriteRead.ino (https://github.com/rnsheehan/ArdForPY ) can be uploaded to the Arduino Micro to enable AC measurements in conjunction with the SparkFun MiniGen
The sketch comprises four sections
  preamble
  setup
  loop
  function definitions

## Slide 62: Arduino Micro AC Sketch
Preamble
  Define constants used throughout the code
  Define commands that tell Arduino Micro to perform some action
  Constants and commands have been made consistent between DC and AC sketches
  Commands are kept simple: write or read
  To keep things simple I have defined 5 commands
    AC read ‘r’
    AC write ‘w’
    DC read ‘l’
    DC write from channel A ‘a’
    DC write from channel B ‘b’
  If anything other than these commands is input an error is thrown

## Slide 63: Arduino Micro AC Sketch
Setup
  Set the baud rate for Serial comms
    https://www.arduino.cc/reference/en/language/functions/communication/serial/begin/
    It’s possible that baud rate can be optimised, but who has the time?
  Tell the SparkFun MiniGen board what to do once it’s powered up
    This set of commands resets the board to a known state
    It requires all connections between SFMG and AM to be correct – REALLY IMPORTANT TO HAVE ALL CONNECTIONS CORRECT OTHERWISE SFMG WON’T WORK
    If setup has executed correctly, and all connections are correct, output from SFMG will be a 1 kHz sine wave with amplitude 1 Vpp DC offset of Vin/2, Vin = 3.3 V

## Slide 64: Arduino Micro AC Sketch
Loop
  Main operating loop for the board
  Loop is written such that it sits and waits for you to enter one of the commands before doing anything
  In the case of SigGenWriteRead.ino there are only three valid inputs
    readCmdStr = r: print current measured voltages from Analog inputs A0, A1
    writeCmdStr = w<val>: change operating frequency of SFMG to <val> Hz
      E.g. w33500: output 33.5 kHz sine wave
    <val> should be a numeric string in the range [100, 3000000], code will force it to either endpoint otherwise
  Any other input will result in printing of ERR_STRING defined preamble
  Arduino IDE has built-in string processing capability
    https://www.arduino.cc/reference/en/language/variables/data-types/stringobject/

## Slide 65: Arduino Micro AC Sketch
Loop
  When readCmdStr is input I currently tell the board to find the max voltage values on A0 and A1
  I then subtract the DC offset value from A0 reading
  It would probably be better practice to tell the board to return max{A0}-min{A0} and max{A1} – min{A1}
  This would avoid any ambiguities that may arise in the use, or otherwise, of DC blocks that may occur
  This is something that needs to be updated

## Slide 66: Arduino Micro AC Sketch
Function Definitions
  Functions are defined after loop, no need for forward declaration
  Only one function is used in SigGenWriteRead: analogVoltageRead
    analogVoltageRead converts the bit-reading at the analog input pin to a voltage value
    analogVoltageRead uses built-in analogRead function
      https://www.arduino.cc/reference/en/language/functions/analog-io/analogread/

## Slide 67: Arduino Micro AC Sketch
Once the sketch has been uploaded the commands w<val>, r can be used to control the device
One way is to open a Serial monitor that talks to the board, using Arduino IDE (Tools -> Serial Monitor) or Putty
The other is to open Serial monitor via LabVIEW
  This has the advantage of enabling data parsing and storage ( the Arduino Micro is a Read-Only file system so it cannot create files )
  AM_Freq_Resp.vi contains all the code needed to implement frequency response characterisation
    Write vi, Read vi, String Processing, Data Formatting etc
    FR loop has been implemented, it is independent of the load attached to SFMG

## Slide 68: Arduino Micro Programming
Arduino IDE can be obtained free of charge from https://www.arduino.cc/en/software
Arduino also have an online language reference library https://www.arduino.cc/reference/en/
Introduction to Arduino: https://learn.sparkfun.com/tutorials/what-is-an-arduino/all
Installing Arduino IDE: https://learn.sparkfun.com/tutorials/installing-arduino-ide
Installing an Arduino Library: https://learn.sparkfun.com/tutorials/installing-an-arduino-library
Installing Arduino Board Definitions: https://learn.sparkfun.com/tutorials/installing-board-definitions-in-the-arduino-ide

## Slide 69: Test Automation with LabVIEW

## Slide 70: Test Automation with LabVIEW
As far as the PC is concerned AM is an addressable serial port, this means we can use NI LabVIEW to talk to the AM board
Commands can be sent and data read using VISA write and read
LabVIEW has significant string processing capabilities built-in, this means that the actual code on the AM can be kept reasonably simple
LabVIEW code for performing automated characterisation is contained in https://github.com/rnsheehan/ArdForPY

## Slide 71: Test Automation with LabVIEW
For DC tests see AM_DC_Test.vi located at https://github.com/rnsheehan/ArdForPY/tree/main/AM_DC_Test%20Folder/MicroControllers
For AC tests see AM_Freq_Resp.vi located at https://github.com/rnsheehan/ArdForPY/tree/main/AM_Freq_Resp%20Folder/MicroControllers
DC and AC tests have several VI in common, common vi are named starting with MuC_****
Context help should be available for each vi in any case

## Slide 72: Acknowledgements
I would like to thank Ms. Lisa Faherty for her help in getting me started with the Arduino Micro, for bringing the SparkFun MiniGen to my attention and for helping me get the SparkFun MiniGen set up in the first place.